## Slide 1
Knowledge Thread 1: Session 1 (Studio 1)
Ama Simons

## Slide 2: This Studio covers
Parallel Input/Output System as a Combinational Digital Lock
Sequential Lock

## Slide 3: What do you need?
3 push buttons
3 330 ohms resistors
3 10kohms resistors
Wires (for connections on your bread-board as well as connections to the MCU)

## Slide 4: Why are we doing this?
Looking ahead to your next lab
Using the Moore Finite State Machine
Parallel I/O System as a Combinational Digital Lock

## Slide 6: Defining the Combinational Digital Lock
States and Inputs:
  2 states – Locked or Unlocked
  2 binary inputs for the code, (only one right code)
  1 binary input to enter the code

## Slide 7: Defining the Combinational Lock
0 or Locked
01
10
1 or Unlocked
X = 111
X = 111
X = 111
X = 111
Binary Inputs
binary value for logic testing
CODE = 11

## Slide 8: Using MCU to Implement
0 or Locked
01
10
1 or Unlocked
X = 111
X = 111
X = 111
X = 111
Binary Inputs
binary value for logic testing
PM2 Load or enter | PM1 Binary value input | PM0 Binary value input
1 | 1 | 1
PN0
D2 ON
PN1
D1 OFF
PN0
D2 OFF
PN1
D1 ON

## Slide 9: Entering the code and load with Push Buttons
We will use push buttons to enter the code
In Lab 1 you wired an active low push button
  Button Pressed = 0
  Button not Pressed 1
In Lab 2 you can use an active high push button
  Button Pressed = 1
  Button not Pressed = 0
PM2 Load or enter | PM1 Binary value input | PM0 Binary value input
1 | 1 | 1

## Slide 10: Active High Push Button with Pull Down Resistor
Circuit Diagram TinkerCad
3 V
330 ohms
10 Kohms
Ground
Input to MCU
LED to TEST
Pull down resistor
Limits the current
330 ohms
10 Kohms
LED to TEST
Input to MCU

## Slide 11: Active High Push Button with a Pull Down Resistor
Real Life
10Kohms
330 ohms
Led to Test
Button
3 V from the Board
0 V from the board

## Slide 12: Exercise 0 (15 mins) : Wire 3 Active High Push Buttons for Inputs
The results of what you should have at the end of the 15 mins is uploaded to your studio table
After you have achieved these results or at the end of 15 mins come back

## Slide 13: Code Run Through
Find our addresses
Turn on need ports etc.
Set digital system to locked =
PN1 | PN0
0 | 1
D2 ON

## Slide 14: Exercise 2: 20 mins
Using the file that is uploaded to your studio table load the program onto your microcontroller and test the combinational lock system
There is a video of the results in your table

## Slide 15: Sequential Lock
States and Inputs:
  More than 2 states
  1 binary input for the sequence
  1 binary input to that loads the data (acts like a clock)

## Slide 16: Defining the Sequential Lock
00 or Locked
01
10
10 or Unlocked
0
SEQUENCE = 11
01 or Locked2
01
1
1
0
1
0

## Slide 17: Using the MCU to Implement
PN0
D2 ON
PN1
D1 OFF
PN1
D1 OFF
PN1
D1 OFF
PN0
D2 ON
PN0
D2 ON
PM0
PM4
Clock or load value

## Slide 18
End